## Slide 1
<number>
SOUTH AFRICAN MEDICAL DEVICE REGULATORY FRAMEWORK
PRESENTATION AT AHWP MEETING
BY
NONKONZO T. MOLAI
DEPARTMENT OF HEALTH – SOUTH AFRICA
28 NOV 2010
Notes: <number>
Minister, DG and colleagues
It is my privilege to present the progress made by the SHP Branch up to date and the planned priorities for 2006/07 to you today.

## Slide 2
<number>
Notes: <number>
My presentation will focus on:
the structure of the branch as an introduction to the presentation
Relevant key strategic priorities and activities for 2005/06
Some progress made during the year up to date
a summary of challenges
An overview of the proposed priorities for 2006/07
I will conclude with some key and cross-cutting issues.

## Slide 3
<number>
Notes: <number>
My presentation will focus on:
the structure of the branch as an introduction to the presentation
Relevant key strategic priorities and activities for 2005/06
Some progress made during the year up to date
a summary of challenges
An overview of the proposed priorities for 2006/07
I will conclude with some key and cross-cutting issues.

## Slide 4: Brief Country Profile
Population: 49.9 Million
Health Expenditure: 8.7% of GDP
Two-tier healthcare system (public & private sector)
South Africa’s Burden of Disease (BoD)
  HIV & AIDS and TB;
  High Maternal and Child Mortality;
  Non-Communicable Diseases
  Violence and Injuries;
Main Goals/outputs
- Increasing life expectancy
- Decreasing maternal and child mortality
- Combating HIV & AIDS as well as STIs and decreasing the burden of disease from tuberculosis
- Strengthening Health System effectiveness focusing on (NHI, Quality improvement, Strengthening Infrastructure incl HT, HR, PHC approach…)

## Slide 5: Medical Devices
SA Major trading partners (EU, USA, Japan - India, China & Brazil growing)
Largely an importing country with a small but growing local medical device manufacturing capacity
Main challenges
- Inadequate system of safety & performance inspection
- No system of equipment recall & hazard notification
- Limited obligations to comply with regulatory requirements
- +/-25% of all medical equipment is unusable or unused
- No regulations to compel industry to provide comprehensive after-sale service
- No post market vigilance system
- Poor maintenance practices (especially in public service)
- General poor management of health technology

## Slide 6
CURRENT STATUS | ADDITION
LEGISLATION Hazardous Substances Act (for Radiation Control and | - The National Health Act provides appropriate base for regulating medical devices - Medicines and Related Substances Amendment Act (72) (which provides for the control of Medicines, MD & IVDD incl. establishment of SAHPRA)
CLASSIFICATION The list could be arbitrary without a unified system. New devices may not be legally included | The international risk-based and rule-based classification system to be adopted
AUTHORIZATION Accepts the CE mark | Conformity assessment with SA national standards and DoH criteria
QUALITY SYSTEM & AUDITING Accepts EU Notified Body assessment. | Local assessment by agencies with SANAS accreditation

## Slide 7
POSTMARKET SURVEILANCE Report product defects | Will include: Problem monitoring & reporting Implant registration Recall procedure Complaint handling Quality system follow-up
CURRENT STATUS | DRAFT REGULATIONS
ESTABLISHMENT LICENSING Governs only vendors for listed electro-medical devices | Includes vendors of all medical devices The concept of License Holder will be applied to all devices
AFTER SALE OBLIGATIONS Only to keep distribution records Notification of product defects or non-compliance Prohibition of modification and repair of listed product | Comprehensive after-sale obligations will be required, including post-market surveillance Also includes service training & support

## Slide 8: LEVEL 1

## Slide 9: Three Levels of Medical Device Regulations
Needs Assessment
Health Technology Assessment (HTA)
Qualified user
Safe/Effective use
Good Management Practice (GMtP)
I
II
III
MARKET
SELECTION
UTILISATION
Market Availability
Classification
Safety & Performance
GHTF Guidelines
Post Market Obligations

## Slide 10: Three Levels of Medical Device Regulations
Needs Assessment
Health Technology Assessment (HTA)
Qualified user
Safe/Effective use
Good Management Practice (GMtP)
I
II
III
MARKET
SELECTION
UTILISATION
Market Availability
Classification
Safety & Performance
GHTF Guidelines
Post Market Obligations
Current Focus on Safety

## Slide 11: Conformity Assessment (Proposed Scheme)
If necessary (e.g. no standard or expertise available)
Documentation requirements
Establishment license
Low risk devices
SANAS ACREDITED
OVERSEAS AGENT
LOCAL ASSESSMENT
National Standards From SSA
SANAS Accredited Assessment Agent
Medium to
High Risk
devices
SA License

## Slide 12: Conformity Assessment (Proposed Scheme)
Mandatory registration of medical devices & IVDDs including their establishments
Risk based Call-up process for listing of those devices already on the market
If necessary (e.g. no standard or expertise available)
Documentation requirements
Establishment license
Low risk devices
SANAS ACREDITED
OVERSEAS AGENT
LOCAL ASSESSMENT
National Standards From SSA
SANAS Accredited Assessment Agent
Medium to
High Risk
devices
SA License
Mutual Recognition Agreements
- Critical Stakeholders (SANAS, SABS)
- AHWP Member States??

## Slide 13: Post Market Obligations on Vendors
Records (e.g. for Traceability)
Mandatory reporting of adverse events
Competent trained maintenance staff
Facilities for maintenance
CE Technicians competence (mandatory registration with the Engineering Council of South Africa for class C&D)
Availability and Quality of Consumables and spares
User training

## Slide 14: Level 2 Focus
Current focus on Safety
Aiming to establish the Health Technology Assessment Agency
Give the Agency a legal muscle

## Slide 15: LEVEL 3

## Slide 16: Focus During Utilization Stage
QM Stds (Essential elements of GMtP) recognised in law and concretized in codes
Requirement to fulfill minimum QM Stds prior to acquisition which include…
- Delivery & inspection
- Inventory, record-keeping
- Installation
- Training
- Mandatory Registration of Clinical Engineers & technicians
- Maintenance (Liability issues)
- Disposal

## Slide 17: Pre-Acquisition Considerations
Availability of qualified users
Reassured source of recurrent operating budget (consumables, labour, parts)?
Confirmed maintenance services & support ?
Adequate environment support ?
Regulatory compliance ?

## Slide 18: Pre-Acquisition Considerations
Are there qualified users in the healthcare facility?
Are maintenance services confirmed?
Are there adequate environment supports e.g adequate
  electrical supplies
  clean water
  clean rooms
  acceptable ambient temperature and humidity

## Slide 19: Device/Equipment Pre-acquisition Questions
Are there qualified users in the healthcare facility?
Are maintenance services confirmed?
Are there adequate environment supports such as adequate electrical supplies, clean water, clean rooms, acceptable ambient temperature and humidity?

## Slide 20: All Device/Equipment Use, Maintenance, Disposal
Only qualified users use medical devices
Policy and procedures are in place for the training of each new user for safe and effective use of medical devices
In-house personnel and facilities, outsourced third party, or a combination of in-house and outsourced services are adequate for the maintenance of medical devices
Policy and procedures are in place for appropriate disposal of used medical devices/equipment

## Slide 21: THANK YOU